## Slide 1
Xylophone Capstone
Musical instrument documentation capstone
Build packet: xylophone
Generated: 2026-05-08
Xylophone Capstone | Slide 1 of 14

## Slide 2
Project Intent
• Ship a parametric, validator-clean, public-readable Mode A build packet for a serious wooden tuned-bar idiophone — small enough to build in one shop session, honest enough about the physics that the predicted frequencies and the measured frequencies will disagree on first cut and the workflow can correct them, structured enough that a marimba follow-on can reuse the family table, the validation rows, the suspension geometry, the SolidWorks master-layout convention, and the empirical-correction guard rules.
Xylophone Capstone | Slide 2 of 14

## Slide 3
Physics Model
• Free-free Euler-Bernoulli transverse beam vibration, first mode:
Xylophone Capstone | Slide 3 of 14

## Slide 4
How To Use This Packet
• Start with design.md for intent and assumptions.
• Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
• Use drawing-brief.md and CAD/CNC folders before machining.
• Print the packet for shopping, shop work, and validation.
Xylophone Capstone | Slide 4 of 14

## Slide 5
File Map
• design.md: Project intent, catalog metadata, assumptions, and validation plan.
• bom.csv: Starter bill of materials with part categories, quantities, drawing refs, and notes.
• sourcing.csv: Supplier/search tracker with specs, price/date fields, lead time, substitutes, and risks.
• cut-list.csv: Rough/final stock sizes, material, grain/orientation, operations, yield, and offcuts.
• drawing-brief.md: Manufacturing drawing and technical product sketch brief.
• assembly-manual.md: Shop-facing sequence, tools, fixtures, safety, tuning, finishing, and maintenance notes.
• validation.csv: Target/measured values, tolerance, environment, result, and tuning/build action log.
• supplier-rfq.md: Supplier email/request-for-quote starter.
Xylophone Capstone | Slide 5 of 14

## Slide 6
Family Spec
note | target_hz | bar_length_in | bar_width_in | bar_thickness_in | hole_pos_low_in | hole_pos_high_in | predicted_f1_hz | predicted_f1_source | wood_species | resonator_l_in_optional | mass_oz_est | notes
C5 | 523.25 | 16.683 | 1.500 | 0.875 | 3.737 | 12.946 | 523.25 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 5.22 | 9.43 | solved L from target_hz
C#5 | 554.37 | 16.208 | 1.500 | 0.875 | 3.631 | 12.578 | 554.37 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 4.86 | 9.16 | solved L from target_hz
D5 | 587.33 | 15.747 | 1.500 | 0.875 | 3.527 | 12.220 | 587.33 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 4.52 | 8.90 | solved L from target_hz
D#5 | 622.25 | 15.299 | 1.500 | 0.875 | 3.427 | 11.872 | 622.25 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 4.20 | 8.65 | solved L from target_hz
E5 | 659.26 | 14.863 | 1.500 | 0.875 | 3.329 | 11.534 | 659.26 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 3.89 | 8.40 | solved L from target_hz
F5 | 698.46 | 14.440 | 1.500 | 0.875 | 3.235 | 11.205 | 698.46 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 3.60 | 8.16 | solved L from target_hz
F#5 | 739.99 | 14.029 | 1.500 | 0.875 | 3.142 | 10.886 | 739.99 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 3.33 | 7.93 | solved L from target_hz
G5 | 783.99 | 13.630 | 1.500 | 0.875 | 3.053 | 10.577 | 783.99 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 3.08 | 7.70 | solved L from target_hz
G#5 | 830.61 | 13.242 | 1.500 | 0.875 | 2.966 | 10.275 | 830.61 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 2.83 | 7.48 | solved L from target_hz
A5 | 880.00 | 12.865 | 1.500 | 0.875 | 2.882 | 9.983 | 880.00 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 2.61 | 7.27 | solved L from target_hz
A#5 | 932.33 | 12.498 | 1.500 | 0.875 | 2.800 | 9.699 | 932.33 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 2.39 | 7.06 | solved L from target_hz
B5 | 987.77 | 12.143 | 1.500 | 0.875 | 2.720 | 9.423 | 987.77 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 2.19 | 6.86 | solved L from target_hz
C6 | 1046.50 | 11.797 | 1.500 | 0.875 | 2.643 | 9.154 | 1046.50 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 2.00 | 6.67 | solved L from target_hz
C#6 | 1108.73 | 11.461 | 1.500 | 0.875 | 2.567 | 8.894 | 1108.73 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.81 | 6.48 | solved L from target_hz
D6 | 1174.66 | 11.135 | 1.500 | 0.875 | 2.494 | 8.641 | 1174.66 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.64 | 6.29 | solved L from target_hz
D#6 | 1244.51 | 10.818 | 1.500 | 0.875 | 2.423 | 8.395 | 1244.51 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.48 | 6.11 | solved L from target_hz
E6 | 1318.51 | 10.510 | 1.500 | 0.875 | 2.354 | 8.156 | 1318.51 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.33 | 5.94 | solved L from target_hz
F6 | 1396.91 | 10.211 | 1.500 | 0.875 | 2.287 | 7.923 | 1396.91 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.19 | 5.77 | solved L from target_hz
F#6 | 1479.98 | 9.920 | 1.500 | 0.875 | 2.222 | 7.698 | 1479.98 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 1.05 | 5.61 | solved L from target_hz
G6 | 1567.98 | 9.638 | 1.500 | 0.875 | 2.159 | 7.479 | 1567.98 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.92 | 5.45 | solved L from target_hz
G#6 | 1661.22 | 9.363 | 1.500 | 0.875 | 2.097 | 7.266 | 1661.22 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.80 | 5.29 | solved L from target_hz
A6 | 1760.00 | 9.097 | 1.500 | 0.875 | 2.038 | 7.059 | 1760.00 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.69 | 5.14 | solved L from target_hz
A#6 | 1864.66 | 8.838 | 1.500 | 0.875 | 1.980 | 6.858 | 1864.66 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.58 | 5.00 | solved L from target_hz
B6 | 1975.53 | 8.586 | 1.500 | 0.875 | 1.923 | 6.663 | 1975.53 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.48 | 4.85 | solved L from target_hz
C7 | 2093.00 | 8.342 | 1.500 | 0.875 | 1.869 | 6.473 | 2093.00 | free-free Euler-Bernoulli f1=1.028(h/L^2)sqrt(E/rho); first-order; Padauk E=12.6GPa rho=745kg/m3 | Padauk | 0.38 | 4.71 | solved L from target_hz
Xylophone Capstone | Slide 6 of 14

## Slide 7
Build Workflow
• Design and assumptions
• Source materials and hardware
• Prepare stock, fixtures, and CNC/laser/lathe setup
• Assemble, tune, finish, and validate
Xylophone Capstone | Slide 7 of 14

## Slide 8
Sourcing And BOM
• BOM gives part categories and drawing references.
• Sourcing tracks search terms, supplier candidates, price/date, lead time, substitutions.
• Visual BOM brief turns the parts list into a presentation-ready image board.
Xylophone Capstone | Slide 8 of 14

## Slide 9
Shop Packet
• Cut list for lumber/sheet/blank planning.
• Assembly manual for away-from-keyboard work.
• Validation sheet for measured dimensions, tuning, pass/fail checks.
Xylophone Capstone | Slide 9 of 14

## Slide 10
Drawings, CAD, CNC
• drawing-brief.md defines required views, dimensions, datums, sketch intent.
• cad/ holds models and design tables.
• cnc/ holds CAM, toolpaths, setup sheets, dry-run notes.
• drawings/ holds PDFs, SVGs, DXFs, drawing exports.
Xylophone Capstone | Slide 10 of 14

## Slide 11
Images And Screenshots
• images/xylophone-hero-placeholder.svg
Xylophone Capstone | Slide 11 of 14

## Slide 12
Validation Plan
• A4 = 440 Hz reference check.
• Tuning targets logged in validation.csv.
• Critical dimensions verified against design sheet and CAD.
• Photos and revision notes after each major step.
Xylophone Capstone | Slide 12 of 14

## Slide 13
Open Risks / Decisions
• TBDs in design sheet and BOM.
• Supplier price/availability not yet verified.
• Generated images marked as concept placeholders.
• Empirical corrections await measured prototype data.
Xylophone Capstone | Slide 13 of 14

## Slide 14
Next Actions
• Replace TBDs with measured/source-backed values.
• Verify live supplier price and availability before buying.
• Export final drawings and visual BOM images.
• Regenerate this deck and print packet after final edits.
Xylophone Capstone | Slide 14 of 14